## Slide 1
DOCKING LAB · OCTOBER 2026
DOCKING LAB · INVESTOR BRIEF
cover capture · this project's own dashboard, 100 m approach
01
/ 16
A spacecraft that
docks itself.
And shows its work.
An LLM plans the manoeuvre, a learned policy advises it, and an independent safety channel gates every command — over real orbital dynamics, in one dashboard.
THE LAST RECORDED RUN
1.945
cm
final port separation
0.004
m/s
relative speed at capture
0
fallbacks
two provider decisions, both applied
Notes: Open on the button: this is a working system, not a concept video.
Say in one breath: an LLM, a learned policy and an independent safety channel fly a 500 kg chaser from 100 metres to a centimetre-class capture — and every claim in this deck traces to a file.
Numbers on screen: 1.945 cm, 0.004 m/s, zero fallbacks — proofs/precision-vertex-docking/checks.json.

## Slide 2
THE PROBLEM
DOCKING LAB · INVESTOR BRIEF
gate defaults · src/app/simulation/safety.py
02
/ 16
The final 100 metres
decide the mission.
Rendezvous is unforgiving: close on a moving target, null your motion down to centimetres, and touch down softly enough to latch.
0.005
m/s
the permitted capture speed at the shared gate — every method, human or learned, is judged against the same number.
One controller per target
A new vehicle or a new port means another hand-tuned control law and another test campaign.
Rehearsal is scarce
On-orbit proximity rehearsal is expensive and rare; ground rigs cannot reproduce contact dynamics or sensor dropouts.
Autonomy nobody can question
A planner a reviewer cannot interrogate cannot be signed off — the capability stalls at the demo stage.
Notes: Frame the pain in plain terms: proximity operations carry the mission risk, every new target restarts the control-law and verification campaign, and autonomy that cannot explain itself never gets certified.
The 0.005 m/s figure is this simulator's shared capture gate (src/app/simulation/safety.py) — present it as the class of tolerance, not as an ISS requirement.

## Slide 3
WHY NOW
DOCKING LAB · INVESTOR BRIEF
planning · src/app/llm/reasoning_agent.py · src/app/llm/tools.py
03
/ 16
Three things got cheap — all at once.
The bottleneck moved. Planning, advice and verification are now implementable in one week of engineering time.
01
Tool-using models
The planner calls measurement tools, previews a manoeuvre before submitting it, and records the alternatives it rejected. Interrogable, not a black box.
Learned advice on a budget
02
An expert-initialized PPO policy trains to 200,704 environment steps on two T4 GPUs and is evaluated on held-out seeds. It advises; it never actuates.
03
Evidence-first engineering
Every run exports configuration, decisions, tool readings, telemetry and SHA-256 hashes — a reviewer re-derives each number instead of trusting a slide.
Notes: The 'why now': the pieces are individually unremarkable, the composition is new.
Each card cites its artifact — the tool loop in src/app/llm/tools.py, PPO evidence in proofs/kaggle-final-seed-42/, exports in proofs/precision-vertex-docking/.

## Slide 4
THE SYSTEM
DOCKING LAB · INVESTOR BRIEF
architecture · src/app/simulation/runner.py · src/app/llm/tools.py
04
/ 16
One dashboard. One closed loop.
PLAN
A planner with six tools
A LangChain planner calls six inspection and submission tools. Vertex AI by default; OpenAI, Groq, OpenRouter and Anthropic selectable.
It measures, checks the gate, previews the manoeuvre, then submits — with a rationale.
ADVISE
A policy that suggests
An expert-initialized PPO advisor supplies a learned proposal — a 4-second lookahead closing vector.
The planner may adopt it, cap it or reject it, and every decision records which, with a reason.
FLY
A controller that never guesses
An LQR controller tracks the accepted target continuously, under per-axis force, torque, acceleration and stopping-distance envelopes on a 500 kg chaser.
Physics never waits for the planner — it keeps stepping while guidance is pending.
AND UNDERNEATH EVERYTHING
An independent safety channel reads simulator truth, enforces the motion and capture gates, and performs fault braking — surviving provider loss and stale sensor data.
Notes: Walk left to right: plan, advise, fly — then the band underneath.
The architectural claim for a technical reviewer: deterministic physics and safety sit outside the planner, so provider latency or failure cannot corrupt the state.
Sources: src/app/simulation/runner.py, dynamics.py, safety.py, src/app/llm/reasoning_agent.py, tools.py.

## Slide 5
CONTROL ARCHITECTURE
DOCKING LAB · INVESTOR BRIEF
lanes · src/app/simulation/runner.py · src/app/llm/rl_advisor.py
05
/ 16
Nothing flies unchallenged.
Four lanes. Only the first two can be wrong.
1
PLANNER
An LLM over a six-tool loop: measure distance, inspect the capture gate, inspect actuators, read the learned proposal, preview a manoeuvre, submit — returning targets, a rationale and the alternatives it rejected.
Vertex AI by default
four providers selectable
2
ADVISOR
Expert-initialized PPO proposes a 4 s lookahead closing vector. The planner may adopt it, cap it or reject it — every decision records which, with a reason.
advice, never authority
3
EXECUTOR
LQR tracking under per-axis force and torque, total thrust, acceleration and stopping-distance envelopes on a 500 kg chaser: 50 N total, 20 N·m per axis, 0.1 m/s² local acceleration.
propellant follows
applied impulse
4
SAFETY CHANNEL
Independent of the planner and the policy. It reads simulator truth, enforces the motion and capture gates, discards expired plans and labels the recovery manoeuvre.
survives provider loss
and stale sensor data
In the recorded run, accepted decisions carried 24.4 s and 22.6 s plan age while the simulation kept advancing.
Notes: The line for engineers: only lanes 01 and 02 can be wrong, and neither can actuate anything directly.
Provider failure produces labelled deterministic guidance, never silence.
Numbers: 50 N, 20 N·m, 0.1 m/s², 500 kg; plan ages 24.4 s and 22.6 s from proofs/precision-vertex-docking/decisions.json.

## Slide 6
LIVE TRACE
DOCKING LAB · INVESTOR BRIEF
verbatim quotes · proofs/precision-vertex-docking/decisions.json
06
/ 16
It argued with its own advisor — and won.
“Adopt the RL short-horizon waypoint at 0.65 m/s: rejected — it creates an unnecessary intermediate stop and underutilizes the 2.0 m/s approach envelope at 100 m range.”
Vertex gemini-3.8-flash · decision 1 of 2 · plan age 24.4 s · applied
“The RL velocity direction aligns well with the line of sight; the short lookahead is rejected to prevent stopping mid-trajectory.”
Vertex gemini-3.8-flash · decision 2 of 2 · range 2.49 m · plan age 22.6 s · applied
WHAT THE RUN RECORDS
2
decisions
0
fallbacks
45.3
° initial error
449
steps of force + torque
Both plans were validated against the state at submission, then re-gated by the safety channel before actuation.
This is the reviewable part: the model states its target, its reason, and the proposal it declined — with the measurement that justified the choice. Short explanations are surfaced; private deliberation is not.
Notes: Slow down here. This slide separates the project from a demo video: quoted decisions with plan age, an applied flag and the rejected alternative, all in proofs/precision-vertex-docking/decisions.json.
The model overrode its learned advisor using the configured envelope — judgment, not improvisation.

## Slide 7
CAPTURE CRITERIA
DOCKING LAB · INVESTOR BRIEF
07
/ 16
Capture is a contract.
All four checks must pass, plus one second of stable alignment and entry into a 5 cm lateral corridor. Manual and automatic capture share the same gate.
RANGE
2
cm
shared gate · max 3 cm
RELATIVE SPEED
0.005
m/s
max 0.01 m/s
ATTITUDE ERROR
1
°
default tolerance
ROTATION RATE
0.01
rad/s
relative, at contact
A stopping-distance envelope brakes the chaser before the near-port zone, then tightens to capture speed. All four checks are satisfied together, not in sequence.
Notes: The gate is code, not convention: safety.py evaluates all four checks plus stability and corridor entry.
The announced capture only fires after server confirmation — the UI cannot claim eligibility during abort or sensor dropout.
Imagery is a real capture from this project's dashboard.

## Slide 8
RESULT
DOCKING LAB · INVESTOR BRIEF
08
/ 16
100 metres to 1.945 cm. Zero fallbacks.
1.945
cm
FINAL SEPARATION
0.004
m/s
SPEED AT CAPTURE
133.6
s
SIMULATED TIME
5×
/ 75.4 s
PLAYBACK / WALL CLOCK
ENVELOPE ACTUALLY USED
max speed 1.999 m/s
max thrust 50.0 N
max accel 0.100 m/s²
gate checks 4 / 4 passed
LLM calls 2 applied
fallbacks 0
Measured telemetry · live Vertex + PPO advisory · one accelerated demonstration at a 2 cm simulated gate
Speed and thrust sat exactly at the configured ceilings — the envelope bound the manoeuvre, not the model's optimism.
Notes: Lead with the constraint, not the number: the chaser used its full configured envelope (2 m/s, 50 N) and still arrived at 0.004 m/s.
Chart from proofs/precision-vertex-docking/approach-curves.png.
Say the scope out loud: one accelerated live demonstration at a 2 cm simulated gate, not a hardware accuracy claim.

## Slide 9
LEARNED ADVISOR
DOCKING LAB · INVESTOR BRIEF
training + evaluation · proofs/kaggle-final-seed-42/ · proofs/kaggle-final-seed-137/
09
/ 16
Fly the expert. Then improve on it.
Reproducible training: expert, cloning, PPO, matched normalisers, held-out seeds.
STEP 01 · THE EXPERT
LQR trajectories
100 expert episodes over the same dynamics.
STEP 02 · THE DEMONSTRATION
Behaviour cloning
50 epochs on normalised observations.
STEP 03 · THE REFINEMENT
PPO fine-tuning
200,704 steps, 8 environments, two T4 GPUs.
HELD-OUT EVALUATION · SEEDS 70000–70049 · 5–80 M STARTS
METHOD
SEED 42
SEED 137
LQR with deterministic planner
50 / 50 docked
50 / 50 docked
PID with deterministic planner
50 / 50 docked
50 / 50 docked
PPO with deterministic planner
50 / 50 docked
50 / 50 docked
LQR with PPO advice — recommended
50 / 50 docked
50 / 50 docked
The archived policy was trained at a 1.25 m gate — these results do not establish centimetre precision. Every 50/50 carries a Wilson 95% interval of ≈92.9–100%.
Notes: Be scrupulous; a technical reviewer will attack this slide.
Say plainly: the archived policy was trained and evaluated at a 1.25 m gate; the notebook packages the 2 cm environment for fresh training.
The value on the table is pipeline reproducibility — expert, cloning, PPO, matched normalisers, held-out seeds.
Sources: proofs/kaggle-final-seed-42/ and -137/.

## Slide 10
EVIDENCE
DOCKING LAB · INVESTOR BRIEF
10
/ 16
Every number has a file behind it.
PROOFS TREE · COMMITTED, HASHED, REVIEWED
kaggle-final-seed-42/ 200,704 training steps
kaggle-final-seed-137/ independent seed
evaluation.json every held-out trial
manifest.json SHA-256 hashes
precision-vertex-docking/ live Vertex + PPO run
decisions.json rationale, rejected options
telemetry.csv range, speed, thrust
code-audit/ 30 + 5 modules audited
verification.json pytest · ruff · proofs
DASHBOARD · DECISION LOG AND EXPORT
Every session exports its configuration, decisions, tool readings and terminal checks — raw material for a replay. Runs that failed are kept beside the successes.
Hashes establish integrity, not endorsement — the reports say so in their own words.
Notes: Hand a reviewer the folder, not a slide. Offer the live dashboard and the export of any session they want to poke at.
If asked what the hashes prove: file integrity, and that the numbers were not edited after the run. They do not certify the simulator.
Verification entry points: python -m pytest; python -m ruff check src tests scripts; python scripts/verify_proofs.py.

## Slide 11
SAFETY & VERIFICATION
DOCKING LAB · INVESTOR BRIEF
11
/ 16
The safety channel trusts only the state.
15
audit findings checked against execution — and fixed
6
of them P1, including fault braking moved to an independent channel
SELECTED P1 CORRECTIONS
Learned advice was silently off by default → an inference probe now enables it, and Reset restores that verified default.
Corrupt policy files passed capability checks → dimensions, normalisation and a finite prediction are validated before a session exists.
Expired provider responses installed braking holds → they are discarded and current-state guidance sustains the approach.
CAPTURE CONFIRMED IN THE DASHBOARD
130 automated tests, ruff clean and a passing production build at the time of the run.
Provider failure and invalid output take a labelled deterministic path.
Safety here is a simulation-time envelope contract, not flight certification — the roadmap starts with latency and sensor models.
Notes: This slide answers 'how do you know it is safe to even run?'. The audit is the strongest artifact in the repository: every finding names its correction and its file.
Say the caveat yourself: simulation-time envelope contract, not flight certification.
Full table: proofs/code-audit/README.md.

## Slide 12
SCOPE
DOCKING LAB · INVESTOR BRIEF
12
/ 16
What this is not.
Stated up front, because the first serious question is: what does this actually prove?
NOT FLIGHT-CERTIFIED
Research software, with no certification of any kind.
LOCAL LINEARISED DYNAMICS
The primary's motion is prescribed, not controlled.
NO CONTACT MODEL
No contact mechanics, structural dynamics or plume interaction.
NO SENSOR ESTIMATION
The safety channel reads simulator truth — not a flight-ready estimator.
DEMONSTRATIONS, NOT RATES
Provider runs are individual live checks, not a success rate.
ARCHIVED POLICY LIMITS
Stored checkpoints were trained at a 1.25 m gate; the 2 cm environment is packaged for fresh training.
PROCESS-LOCAL SESSIONS
Four active and 32 retained sessions in memory, no authentication.
FUEL AND GEOMETRY ARE ASSUMED
Thruster efficiency, lever arm and inertias are editable simulator assumptions.
Notes: Do not skip this slide. For any technical audience it is the credibility purchase: you are disclosing the same limits their reviewers would find.
It also points the conversation at what a partner can change — their propagator, their sensor model, their latency budget.
Sources: proofs/README.md, proofs/code-audit/README.md, README.md.

## Slide 13
INTEGRATION
DOCKING LAB · INVESTOR BRIEF
interfaces · src/app/llm/tools.py · src/app/simulation/safety.py
13
/ 16
Bring your vehicle. Keep the loop.
YOU SUPPLY
A reference vehicle
Mass properties, thruster and torque limits, propellant model, port geometry, capture tolerances.
Your dynamics
Propagator or relative-motion model, attitude coupling, actuator response.
A mission profile
Start corridor, approach constraints, abort criteria, and sensor or timing reality.
WE KEEP
The planner contract
The same six tools, so plans stay inspectable and comparable across vehicles.
The safety contract
An independent gate over your limits, evaluated on your state estimates.
The evidence pipeline
Decisions, telemetry and hashes in one shape, so reviewers read one format.
SWAP POINTS
dynamics — replace Clohessy–Wiltshire with your propagator controller — replace LQR with your GNC law policy — plug your own policy into the advisor slot, it stays advisory
Notes: This is the commercial slide. Do not sell a black box; sell the interface and the evidence format.
The ask follows naturally: one vehicle model and one mission profile, and we re-run the reference scenarios on your dynamics.
Interfaces: src/app/llm/tools.py, src/app/simulation/safety.py, src/app/api/routes.py.

## Slide 14
ROADMAP
DOCKING LAB · INVESTOR BRIEF
14
/ 16
From simulator to qualification.
Three phases, proposed with a partner — none has started.
PHASE 01
Partner dynamics
Plug a partner propagator and actuator model in, re-run the reference scenarios, and publish a paired comparison against the current stack.
Exit: the same capture gate passed on partner dynamics.
PHASE 02
Hardware in the loop
Real flight-computer timing, sensor models and injected comms latency — then verify that stale plans are discarded and recovery stays bounded.
Exit: latency-bounded replanning demonstrated.
PHASE 03
Qualification pack
Traceability from requirement to scenario to telemetry to hash, with failure cases retained and a reviewer-runnable bundle.
Exit: an independent reviewer reproduces a claim unaided.
What stays constant across all three phases: the gate that decides what counts as capture, the six tools the planner may call, and the evidence format a reviewer reads. The vehicle underneath them is yours.
Notes: Phases are proposals, not commitments — say so explicitly and let the partner choose the order. Most aerospace teams start with phase 02, because latency is their real worry.
If asked about timeline or cost: that is a scoping conversation, not a number on this slide.

## Slide 15
THE ASK
DOCKING LAB · INVESTOR BRIEF
pilot scope · draft for partner discussion
15
/ 16
One vehicle model. One mission profile.
A PILOT NEEDS FROM YOU
A reference vehicle
Mass properties, thruster limits, port geometry, capture tolerances.
A mission profile
The scenario you would actually fly, and the failure cases you care about.
An evaluation owner
Someone who will tell us the run is wrong and why. That is the fastest route to a defensible result.
YOU GET BACK
Your scenarios, re-run
The reference captures on your dynamics, with the same gate, the same tools, the same telemetry.
A paired comparison
Your controller against the current stack on identical seeds, reported with intervals.
An evidence bundle
Decisions, tool readings, telemetry and hashes — including the runs that did not work.
Everything in this deck is reproducible from the files in proofs/ — including the failures.
Notes: Adapt the closing sentence to the room before presenting: name the specific team and vehicle you want to fly.
If they push on maturity, concede it and redirect: the loop runs end to end today with an audit trail; what changes with them is the vehicle model and the mission profile.
Do not quote a price or a schedule from this slide.

## Slide 16
DOCKING LAB
DOCKING LAB · INVESTOR BRIEF
16
/ 16
Point it at
your vehicle.
The loop already runs end to end: planner, advisor, executor, safety channel, dashboard and evidence bundle.
WATCH THE RUN
loom.com/share/fc396b5ea4f344659464c48dba367314
OPEN THE EVIDENCE
proofs/ · dashboard at 127.0.0.1:8000 · API docs at /docs
Contact: [ name · email ] — replace before sending
Notes: Close by handing over the artifacts, not by summarising: offer the live dashboard, the proofs folder, and the exported session of any run they want to audit.
Replace the placeholder contact line before sending this deck out.
Demo link as published in README.md.